## Slide 1
Programming Project – Part 1
Softwaredevelopment for Industrial Robotics
Marcel Grotzke, Gabriel Kögler, Henri Hamann 19.12.2013

## Slide 2: Table of content
1. Fundamentals
2. Solutions
2.1 Kinematics
2.3 Point to point movement
2.4 Linear movement
2.5 GUI settings

## Slide 3: 1. Fundamentals - Programming approach (1)
Basic Problem:
Offset between zero configuration and initialization configuration
init config state: zero config state:
Offset in every calculation (IK, DK, …)
Offset even in angle constrains
default
given by data sheet

## Slide 4: 1. Fundamentals - Programming approach (2)
“Two Worlds”: OpenRave World ↔ calculation world
two trigger: AddOffsetToAngles() – our angles to openRave
SubstractOffsetToAngles() – openRave to our angles
def AddOffsetToAngles(arr_angles):
new_arr_angles = np.array
(
[
float(arr_angles[0])-np.pi/2,
-1 * float(arr_angles[1])-np.pi/2,
-1 * float(arr_angles[2])+np.pi/2,
float(arr_angles[3]),
-1 * float(arr_angles[4]),
float(arr_angles[5])
]
)
return new_arr_angles
Offset

## Slide 5: 1. Fundamentals – Code structure
“Two Worlds”: OpenRave World ↔ calculation world

## Slide 6: 2. Solution – Kinematics
PSEUDOCODE: CalculateDirectKinematicsTransformation(dofValues,point,origin,destination):
for i in range ( origin, destination ):
current_cs = destination - i - 1 + origin
angle = dofValues [current_cs – 1 ]
nextMatrix = GetTransformationForDh ( GetDhForJoint(angle,current_cs ))
point = nextMatrix * point
return point
Direct Kinematics:
starting with the last cs
get DH-parameters and use DH-transformation matrix
Calculate transformation to next cs

## Slide 7: 2. Solution – Kinematics
PSEUDOCODE:
CalculateInverseKinematics ( tcp ):
Set wrist point offset;
Calculate wp in CS0;
Transformate wp in CS1;
SolutionsAngleOne = Calculate AngleOne;
for both: SolutionsAngleOne:
Transformate wp in CS2;
SolutionsAngleTwo = Calculate AngleTwo;
        for both: SolutionsAngleTwo:
        Transformate wp in CS3;
        SolutionsAngleThree = Calculate AngleThree;
        Calculate both wrist orientation solutions;
Inverse Kinematics
Adopted from own presentation

## Slide 8: 2. Solution – PTPMovement
def PTPtoConfiguration ( start_cfg, target_cfg, motiontype ):
:param start_cfg: Current axis angle of the robot
:param target_cfg: Target angle of the robot
:param motiontype: asynchronous, synchronous,
:returns: Array of angles of interpolated path
# calculation of step number
step_size = np.int(math.ceil(total_time * calc_frequency))
# step calculation
delta_angle = sign[j] * current_V[j,1] * time_step
trajectory[i,j] = trajectory[i-1,j] + delta_angle
Base functionality | Adv. functionality
Calculates new angles | Path interpolation
Trapezoide velocity profile | Velocity watching
Characteristics
No singularity handling needed
Velocity profile equations the same as in the lecture
Profile´s endpoint always is set to the movement´s endpoint
Velocity profile is not exact match with trapezoide profile

## Slide 9: 2. Solution – LINMovement
PSEUDOCODE:
LINtoConfiguration ( start_cfg, target_cfg, max_vel, max_acc ):
Calc start and end point with direct kinematics;
Calculate velocity profile{
calc time and distance for one acceleration phase
calc distance and time for the constant velocity movement
}
# Go through path from start till one step before end;
for i in range ( 0, end-1 ):
calc target point for the current step i with velocity profile;
calc inverse kinematics solutions for current step i;
select nearest solution and check for singularities{
singularity if angles exceed maximum velocity;
save position of singularity and type;
}
Set last step to end point;
select nearest solution and check for singularities();
HandleSingularities();
CheckAngleConstraints();
return finished_trajectory;

## Slide 10: 2. Solution – GUI Settings
Path visualization
Force robot movement in case of singularities for LINMovement
Show interpolated points
Toggle server communication output

## Slide 11: Many thanks for your attention!

## Slide 12: bibliography
    OpenRave logo from http://en.wikipedia.org/wiki/OpenRAVE