## Slide 1
Programming Task 2:
Spline Movement
Softwaredevelopment for Industrial Robotics
Marcel Grotzke, Gabriel Kögler, Henri Hamann 30.01.2014

## Slide 2: Table of content
(x0, y0)
(x1, y1)
(x2, y2)
(x3, y3)
(x4, y4)
(x5, y5)
1. Fundamentals
2. Spline Approximation
3. Spline Interpolation

## Slide 3: 1. Fundamentals – What are splines?
Origin:
First reference in 1946 [1]
Suitable to describe curved lines → CAD (curves & freeform surfaces)
  i.e. rollercoaster, automobile and shipbuilding, high-speed railways
Definition:
      k knots1 as base
      k-1 continuous, smooth, polynomial segments of degree2 n
      commonly used splines with degree=3 (cubic) → ax3+bx2+cx+d
1 knot = Knotenpunkt, o. Stützpunkt
² degree= Grad
order = 1
order = 2
order = 3
polynomial segments (black),
like ax3 + bx2 + cx + d (cubic)
knots
(red)

## Slide 4: 1. Fundamentals – Splines have to be…
…continuous:
Function plot does not jump
  (to get an ongoing spline)
…smooth:
every argument is calculable
(no infinity1/overshooting)
…differentiable:
need for calculating the spline conditions
1 Unendlichkeit

## Slide 5: 1. Fundamentals - Why Splines?
Typical Problem: Set of data points
→ ad hoc approach: one (global) polynomial passing every point
But: Increasing number of points means increasing error at interval boundary, too.
→ better use another interpolation technique, like i.e. spline interpolation
Increased number
of data points
Example: Runge Function [2]
Notes: Typical Problem: Given set of data points from a series of measurements which is used to process a progression
→ naïve approach: one (global) polynomial which interpolates every single point.

## Slide 6: 1. Fundamentals – Splines can…
…interpolate the given input points:
The given input points are part of the spline.
…approximate the given input points:
The given input points are not part of the spline (i.e. b-spline).
1 unendlich
Interpolation with a cubic spline.
Approximation with a cubic b-spline.
[2]
[2]

## Slide 7: 2. Spline Approximation - B-Spline
Approach:
Linear combination of all segments:
  (1)
With:
Given: n+1 control points D = (d0…dn) (so called de Boor points)
Basis function Ni,k(t)
Order k (degree = k-1)
Time variable t represents the position on the spline
Knot vector ti = (t0,…,tn,…tn+k) (mathematical construct)
Feature:
De Boor points influence spline´s shape

## Slide 8: 2. Spline Approximation - B-Spline
Single polynomial:
Calculated with recursive equation
Order k is a sum of two basis functions with Order k-1
recursive definition:
(2)
Workaround:
Calculate the segments considering the knot vector ti= (t0,…,tn,…tn+k)
for k>1 and i=0,…,n

## Slide 9: 2. Spline Approximation - B-Spline
order 1
order 1
order 2
- b-spline of order k = 2
- polynom of degree 1

## Slide 10: 2. Spline Approximation - B-Spline
order 2
order 2
order 3
- b-spline of order k = 3
- polynom of degree 2

## Slide 11: 2. Spline Approximation - B-Spline
order 3
order 3
order 4
- b-spline of order k = 4
- polynom of degree 3

## Slide 12: 2. Spline Approximation - B-Spline
Knot vector ti:
ti = (t0,…,tn,…tn+k) condition: ti <= ti+1
Uniform knot vector: ti = ti-1 + delta_t (delta_t = constant)
example: delta_t = 1; ti = (t0, t1, t2, t3) = (0, 1, 2, 3)
Non-uniform: delta_t != constant
knot vector represents a wheigt for the basis functions
Factorises the influence of the
de Boor points

## Slide 13: 2. Spline Approximation - B-Spline
Demonstration
of B-spline movement

## Slide 14: 3. Spline Interpolation
System of equations: every segment has one equation!
k knots & order=n → (k-1) polynomial equations with (n+1) variables.
→ total amount of variables = (n+1) * (k-1).
      → with order = 3 → ax3+bx2+cx+d → n=4. (our case)
      → amount of variables = 4(k-1) = 4k-4
      → need for conditions to solve system of equations.
Conditions: Are given by spline´s behavior!
Every knot is part of one segment → pi(xi)=yi → k conditions
Segment´s contact points → pi(xi+1)=pi+1(xi+1) → k-2 conditions
Same in first derivation → pi´(xi+1)=pi+1´(xi+1) → k-2 conditions
Same in second derivation → pi´´(xi+1)=pi+1´´(xi+1) → k-2 conditions
(4k-6) < (4k-4) → we still need two conditions!
Last two conditions:
Define the behavior at the spline´s start and end point (i.e. slope)
Arbitrary decision → p0´(x0)=0 & pk´(xk)=0

## Slide 15: 3. Spline Interpolation
With polynomial si between point (xi, yi) and point (xi+1, yi+1)
→ only one polynomial is active for one input
Length of the interval hi = xi+1 – xi, where polynomial si is “active”

## Slide 16: 3. Spline Interpolation
Calculation of parameter ai, bi, ci and di through curvature ki
 curvature is second derivative of a function
- Through conditions for spline we can derive this function
 this leads to a tridiagonal linear equation system

## Slide 17: Many thanks for your attention!

## Slide 18: bibliography
    Schoenberg: Contributions to the problem of approximation of equidistant data by analytic functions, Quart. Appl. Math., vol. 4, pp. 45–99 and 112–141, 1946.
    Wikipedia: Polynominterpolation. Abgerufen am 25.01.14.
    Wikipedia: Spline. Abgerufen am 18.01.14.
    Moritz Lenz: Splinefunktionen und ihre Anwendung. 2003.
    Schneider: Splines. TU Chemniz. Gefunden auf http://www-user.tu-chemnitz.de/~uro/teaching/SS2002-numerik/misc/Splines.pdf. Abgerufen am 15.01.2014.
    Theisel: Computer Aided Geometric Design: B-Spline. Visual Computing, University of Magdeburg. 2013.

## Slide 19: A. Spline Approximation - B-Spline
Another approach:
Spline with degree=n is a linear combination from 2 splines with degree=n-1 → recursive defintion.
→ input: {Set of points | (xi,yi,zi)}

## Slide 20: A. Fundamentals – Splines definition
Piecewise polynomial calculation of data set {(xi, yi), i = 0, 1, …, n}