## Slide 1
Robot Locomotion – An Introduction
Softwaredevelopment for Industrial Robotics
Marcel Grotzke, Gabriel Kögler, Henri Hamann

## Slide 2: Structure of presentation
1 – Introduction to locomotion
2 – Core issues of locomotion
2.1 – legged locomotion
2.2 – wheeled locomotion
2.3 – comparision of locomotion mechanisms
3 – Outlook to locomotion research

## Slide 3: Introduction to locomotion
Manipulation
Robot fixed
Object is moved
Locomotion
Environment fixed
Robot is moved
Notes: Both concepts
actuators
Generation of interaction forces
motors, pneumatics or hydraulics
Body extensions: arm <-> leg

## Slide 4: Introduction to locomotion
Salamandra
Meshworm
[B1]
[B2]
[B3]
[B4]
Notes: sliding: can swim
Crawl: flexible metal wire -> robust

## Slide 5: Introduction to locomotion
Mini Whegs
WildCat
[B5]
[B6]
[B7]
[B8]
Notes: - jumping: wheeled-legs, winged-legs -> stretch spring
- running: boston dynamics, 26 km/h

## Slide 6: Introduction to locomotion
Asimo
Pioneer
?
[B9]
[B10]
[B11]
Notes: -Walking: use human environments, sidewalk/stairs
-Wheeled: no known counterpart in nature, rolling polygon approximates walking

## Slide 7: Why do we need mobile robots?
Do things which static robots can not do!
[B12]
[B13]
Notes: -Robotic vacuum cleaner Roomba
-Autonomous mower robomaw
-Sell values -> comfort, safe time
-2012 3mio. robots

## Slide 8: Where do we need them?
Daily life  e.g. home, medical facilities, nursing, entertainment
[B14]
Notes: - Caesare

## Slide 9: Where do we need them?
Industry  e.g. carry heavy loads, logistics
[B15]
Notes: - kiva

## Slide 10: Where do we need them?
Extreme environments  e.g. dangerous working places, disaster zones, war zones
[B16]
Notes: - Curiosity

## Slide 11: Core issues of locomotion (1)
Stability
Maneuver-ability
Controll-ability
Major trade-off
Statically-stable → center of gravity lies inside the support pattern
Number of manipulateable DOFs
how “easy” the robot is to
control to achieve the desired motion
Notes: What is to do, to become statically-stable
How “easy” the robot is to control to achieve the desired motion
Amount of manipulateable DOFs

## Slide 12: Core issues to locomotion (2)
Type of environment
Structure
Medium
Stability
Number and geometry of contact points
Static/dynamic stability
Inclination of terrain
Friction
Center of gravity
Angle of contact
Velocity
Energy efficiency
Degrees of freedom
Characteristics of contact

## Slide 13: Legged Locomotion (1)
… series of point contacts between the robot and the ground
Quality of ground between point contacts do not matter
Properties:
→ Adaptability and maneuverability
in rough terrain
→ Potential to manipulate objects
in the environment
→ High power consumption and
mechanical complexity
Important issues:
→ Maneuverability vs. energy,
control and mass
→ Stability during walking
Atlas, bipedal robot, Boston Dynamics, 2013 [Q3]
Mantis hexapod walking machine, micromagic systems, 2009 [B17]

## Slide 14: Legged Locomotion (2)
The leg
Adding joints = adding degrees of freedom (DOF)
Adding DOF =
→ increasing maneuverability
→ increasing power consumption and weight of the robot
→ controlling becomes more complex
Minimum of 2 DOF required for moving leg forward:
→ a lift and a swing motion
3 DOF for each leg in most cases
→ travel in rougher terrain
→ do more complex manoeuvres
Example of a leg with 3 DOF [Q1]

## Slide 15: Legged Locomotion (3)
Stability during walking – static/dynamic stability
During walking some legs are lifted
–Thus loosing stability?
The fewer legs the more complicated becomes locomotion
→ At least 3 legs are required for static stability
Static walking requires at least 6 legs
→ more complex controlling,
→ higher weight,
→ higher power consumption
Bipedal robots are just dynamically stable
→ continuous balance-correcting is needed
Static walking with 6 legs [Q1]

## Slide 16: Wheeled locomotion (1)
Basic
Most appropiate solution for many applications
Most popular locomotion mechanism
Simple mechanical implementation
Easy balance
Very high efficiency ratings
Size of wheels can compensate
environmental constrains
[B18]

## Slide 17: Wheeled locomotion (2)
Stability
3 wheels always stable
2 wheels can be stable
Environment
Biggest limitation → best on planar surfaces
Wheel size compensate environmental contrains
Velocity
Fastest movement
Energy efficiency
Wheels use simple mechanics → best e.e., but limited to planar surf.
Degrees of fredom
Omnidrive → 3DOFs
Need more, need special mechanisms

## Slide 18: Wheel types and DOF
Standard wheel
    2DOFs: Rotation around wheel axe (1) and contact point (2)
Castor wheel
    2 DOFs: Roation around wheel axe (1)
    and contact point (with offset)(2)
Swedish wheel
  3 DOFs: Rotation around wheel axe (1), contact point (2)
  and rollers (3) → omnidirectional
Ball / spherical wheel
difficult technical realization → omnidirectional

## Slide 19: Comparision walking ↔ rolling
Core issue | Walking | Rolling
Stability | - | +
Environment | ++ | --
Velocity | - | ++
Energy efficiency | - | +
Degrees of freedom | + | -
At least 2 wheels can be stable (suspension)
Legs don´t be limited to environement
Wheels move faster (legs still on research)
Energy efficiency depends on reference
Legs can move upward (but complex)

## Slide 20: Outlook to locomotion: Walking Robots from Boston Dynamics
BigDog
Rough-terrain quadruped
robot
Runs at ~6.4km/h
[removed video]
[Q2]
Climbs slopes up to
35 degrees
Carries ~154kg
Funded by DARPA

## Slide 21: Outlook to locomotion: Omni-Crawler
From Osaka University (2009)
Active Omnidirectional movement
Crawler → big load capacities
[B19]

## Slide 22: Outlook to locomotion: VelociRoACH
University of California, Berkeley (2013)
Closed kinematic chain
→ only one engine required!
Speed: 10km/h
Weight: 30g
Length: 10cm
→ 27 body length / sec
[B20]

## Slide 23: Many thanks for your attention!

## Slide 24: Sources
[Q1] Siegbart, Nourbakhsh: Introduction to Autonomous Mobile Robots. Massachusetts Institute of Technology, 2004.
[Q2] Marc Raibert, Kevin Blankespoor, Gabriel Nelson, Rob Playter
and the BigDog Team : BigDog, the Rough-Terrain Quaduped Robot.
Boston Dynamics, Waltham.
[Q3] http://www.bostondynamics.com Stand: 25.10.2013
[Q4] Martin Buehler: Dynamic Locomotion with One, Four and Six-Legged Robots. ARL, Centre for Intelligent Machines, McGill University Montreal.
[Q5] Fukuda, Hasegawa, Sekiyama, Aoyama: Multi-Locomotion Robotic Systems. 2012.
[Q6] Sven Böttcher: Principles of robot locomotion.
[Q7] K. Tadakuma, R. Tadakuma, Nagatani, Yoshida, Iagnemma: Crawler Mechanism with Circular Section to Realize a Sideling Motion. IEEE/RSJ 2008.
[Q8] Haldane, Peterson, Bermudaz, Fearing: Animal-inspired Design and Aerodynamic Stabilization of a Hexapedal Millirobot.

## Slide 25: Image sources
[B1] http://upload.wikimedia.org/wikipedia/commons/f/fe
/Fierce_Snake-Oxyuranus_microlepidotus.jpg
[B2] http://biorob.epfl.ch/files/content/users/179700/files/private
/imports/importInto_ContentContainerList_469885_20110110155706.JPG
[B3] http://1.bp.blogspot.com/-R4EnpcDKpIE/Tvn3Qth8RvI/AAAAAAAACTQ/cXWhSaPwGQc/s1600/Raupe%2BSchwalbenschwanz.jpg
[B4] http://www.digitaltrends.com/wp-content/uploads/2012/08/meshworm.jpg
[B5] http://cdn.orkin.com/images/cockroaches/brown-cockroach-illustration_912x762.jpg
[B6] http://www.realclearscience.com/images/wysiwyg_images
/miniwhegs.png
[B7] http://www.australian-shepherd.kunstvirus.de
/fotos/aussietreffen/treffen0509/attend19.jpg
[B8] http://www.technocrazed.com/wp-content/uploads/2013/10/WildCat-Boston-Dynamics-Robot-Cat-gallops-at-26-Km-per-hr-2.jpg
[B9] http://p4.focus.de/img/gen/B/X/HBBX16Ja_Pxgen_r_300xA.jpg
[B10] http://www.diseno-art.com/images/asimo-walk.jpg
[B11] http://www.cyberbotics.com/dvd/common/doc/webots/guide
/png/pioneer3at_real.png

## Slide 26: Image sources
[B12] http://3.bp.blogspot.com/-OmYtY35FJ2w/T_Yd2RxtFoI
/AAAAAAAAAQU/Ph-MTZCFZeM/s1600/iRobot-Roomba-532.jpg
[B13] http://www.eder-kommunal.de/export/sites/www.eder-kommunal.de/images/gartentechnik/robomow_garten.jpg
[B14] http://www.volksstimme.de/_em_daten/_cache/image/vsm
/0xUmFuZG9tSVYwMTIzNDU2N2PYf+iPAwGxSgUrvg0eJ0vaXlWreOoPI80Y2Y05M5xMmmpMwnOeDKdnP5sy3D9po7NgY4aLTXfT2g9kfKYo9Vla87QITqW6MqWjgEFySKum.jpg
[B15] http://www.hizook.com/files/users/3
/kiva_systems_robot_warehouse_2.jpg
[B16] http://upload.wikimedia.org/wikipedia/commons/d/d8
/NASA_Mars_Rover.jpg
[B17] http://hackedgadgets.com/wp-content/uploads/2013/03/Mantis-Hexapod-Walking-Machine-by-Matt-Denton-_6.jpg Stand: 25.10.2013
[B18] http://www.kuka-omnimove.com/NR/rdonlyres/722C49C4-7E16-4407-9319-703ED52D6F9A/0/H_KUKA_omniMove_03.jpg
Stand: 27.10.2013
[B19] http://assets.inhabitat.com/wp-content/blogs.dir/1/files/2013/01/VelociRoACH-UC-Berkeley-Biomimetic-Millisystems-Lab-Duncan-Haldane-Robot-Close.jpg
Stand: 25.10.2013
[B20] http://www-hh.mech.eng.osaka-u.ac.jp/robotics/Omni-Crawler_e.html Stand: 25.10.2013

## Slide 27: Appendix: swedish wheel
Omnidirectional, but passiv
4 engines needed
passive rollers